## Slide 1
NETCONF by Example
v1.0 (2015-10-05)

## Slide 2: Overview and Objectives
This presentation uses a set of common configuration management tasks to walk through the main features of the NETCONF protocol.
After this presentation, you should be able to:
Obtain desired configuration attributes from a device using NETCONF
Configure a network device using NETCONF
Understand NETCONF transactions

## Slide 3: NETCONF Layering Model
Operations
<get>
<get-config>
Content
Configuration
data
Notification
data
Messages
<rpc>
<notification>
Secure
Transport
ssh
NETCONF
Layer
Example
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<edit-config>
<config>
...Content...
</config>
</edit-config>
</rpc>

## Slide 4: NETCONF Datastores
Configuration loaded by the device at startup
Complete and active configuration
Working copy to manipulate with no impact on current configuration
Candidate
(:candidate)
Running
Startup
(:startup)
<copy>
<commit>
<copy>

## Slide 5: Basic NETCONF Session
<hello>
Capabilities Exchange
Perform operations
End session
client
server
<rpc> <rpc-reply>
<close-session>/<kill-session>
...

## Slide 6: Capabilities Exchange - Hello
<?xml version="1.0" encoding="UTF-8"?>
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.1</capability>
</capabilities>
</hello>
<?xml version="1.0" encoding="UTF-8"?>
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.1</capability>
<capability>urn:ietf:params:netconf:capability:writable-running:1.0</capability
<capability>urn:ietf:params:netconf:capability:candidate:1.0</capability>
...
</capabilities>
<session-id>5</session-id> </hello>
Notes: DEMO NOTE: 01_cmd-hello.py and 01_cmd-hello.xml applies here

## Slide 7: Some Terminology
Operation: A specific remote procedure call, as used within the NETCONF protocol
Operations have parameters
Parameters may have attributes
<rpc message-id="101” xmlns=”urn:ietf:param <get>
<filter type="subtree">
<top xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces"; <interfaces>
</interfaces>
</top>
</filter>
</get>
</rpc>
1
2
3

## Slide 8: Getting Data
We will use:
The <get> operation to get the configuration and operational data in a datastore
The <get-config> operation to get only the configuration data in a datastore
How do I get all configuration and operational data?

## Slide 9: Example of using the <get> operation
Obtaining All Data from device
<rpc message-id="1" xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<get/>
</rpc>
<rpc-reply message-id="1“ xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<data>
<!-- ... entire set of data returned ... -->
</data>
</rpc-reply>
<get>
<data>

## Slide 10: More Realistic <get> Response
<rpc-reply message-id="1" xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<data>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>eth0</name>
<type xmlns:ianaift="urn:ietf:params:xml:ns:yang:iana-if-type">ianaift:ethernetCsmacd</type>
<enabled>true</enabled>
<ipv6 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip">
<address>
<ip>2001:db8:c18:1::3</ip>
<prefix-length>128</prefix-length>
</address>
</ipv6>
</interface>
<interface>
<name>eth1</name>
<type xmlns:ianaift="urn:ietf:params:xml:ns:yang:iana-if-type">ianaift:ethernetCsmacd</type>
<enabled>true</enabled>
<ipv6 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip">
<address>
<ip>2001:db8:c18:2::1</ip>
<prefix-length>128</prefix-length>
</address>
</ipv6>
</interface>
</interfaces>
</data>
</rpc-reply>
<data>
Notes: DEMO NOTE: 02_cmd-get.py and 02_cmd-get.xml applies here

## Slide 11: Filtering Data
We will use:
The <get> or <get-config> operations
The <filter> parameter to select a particular subtree in the reply
How do I filter to get data for just one interface instead of all?

## Slide 12: Example of Filtering Data
<rpc message-id="101” xmlns=”urn:ietf:param <get>
<filter type="subtree">
<top xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces"; <interfaces>
</interfaces>
</top>
</filter>
</get>
</rpc>
Return just the interfaces list
<rpc message-id="1" xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<get>
<filter xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interfaces>
<interface>
<name>eth0</name>
</interface>
</interfaces>
</filter>
</get>
</rpc>
Return the configuration data for just the eth0 interface

## Slide 13: Reply to a filtered <get> on leaf
<rpc-reply message-id="1" xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<data>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>eth0</name>
<type xmlns:ianaift="urn:ietf:params:xml:ns:yang:iana-if-type">ianaift:ethernetCsmacd</type>
<enabled>true</enabled>
<ipv6 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip">
<address>
<ip>2001:db8:c18:1::3</ip>
<prefix-length>128</prefix-length>
</address>
</ipv6>
</interface>
</interfaces>
</data>
</rpc-reply>
<data>
Notes: DEMO NOTE: 03_cmd-get-filter.py, 03_cmd-get-filter.xml applies here for the subtree filter, and 04_cmd-get-filter-name.py and 04_cmd-get-filter-name.xml applies here for filter by name

## Slide 14: Manipulating Data
Example: Enabling and configuring the IPv6 address for an interface
We will use:
The <edit-config> operation to edit the datastore content
  The <target> parameter to specify the datastore,
The <commit> operation to commit the candidate datastore content to the running datastore
How do I manipulate configuration?

## Slide 15: Using <edit-config>
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id="1”>
<edit-config>
<target> ...Spcecify the data store to edit ... </target>
<config> ... Provide the desired configuration to write ... </config>
</edit-config>
</rpc>

## Slide 16: Example: Enabling the Interface
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id="1">
<edit-config>
<target>
<running/>
</target>
<config>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>eth0</name>
<type xmlns:ianaift="urn:ietf:params:xml:ns:yang:iana-if- type">ianaift:ethernetCsmacd</type>
<enabled>true</enabled>
</interface>
</interfaces>
</config>
</edit-config>
</rpc>
Notes: DEMO NOTE: 05_cmd-enable-interface.py and 05_cmd-enable-interface.xml applies here

## Slide 17: Using <edit-config> on candidate
Requires :candidate capability
Clear Candidate
Edit Candidate
Commit
<rpc>
<delete-config>
<target><candidate/></target>
</delete-config>
</rpc>
<rpc>
<edit-config>
<target>
<candidate/>
</target>
<config>
...New Configuration...
</config>
</edit-config>
</rpc>
<rpc>
<commit\>
</rpc>

## Slide 18: Example: Adding IPv6 Address
<rpc message-id="1" xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<edit-config>
<target>
<candidate/>
</target>
<config>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>eth0</name>
<ipv6 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip">
<address>
<ip>2001:db8:c18:1::3</ip>
<prefix-length>128</prefix-length>
</address>
</ipv6>
</interface>
</interfaces>
</config>
</edit-config>
</rpc>
...and then commit
Notes: DEMO NOTE: 06_cmd-add-ipv6-address-commit.py and 06_cmd-add-ipv6-address-commit.xml applies here

## Slide 19: Locking
We will use:
The <lock> operation to lock a datastore
The <delete-config> operation to clear the datastore
The <edit-config> operation to edit the datastore content
The <commit> operation to commit candidate to running
The <unlock> operation to lock a datastore
I don’t want others to change the configuration while I’m editing it!

## Slide 20: Locking the Running Datastore
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id="1">
<lock>
<target><running/></target>
</lock>
</rpc>
Lock Datastore
Clear Candidate
Edit Candidate
Commit
Unlock Datastore

## Slide 21: Clear the Candidate Datastore
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id="3">
<delete-config>
<target>
<candidate/>
</target>
</delete-config>
</rpc>
Lock Datastore
Clear Candidate
Edit Candidate
Commit
Free Datastore

## Slide 22: Edit the Candidate Datastore
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id="4">
<edit-config>
<target>
<candidate/>
</target>
<config>
... Configuration data...
</config>
</edit-config>
</rpc>
Lock Datastore
Clear Candidate
Edit Candidate
Commit
Free Datastore

## Slide 23: Commit the Candidate to Running
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id="5">
<commit/>
</rpc>
Lock Datastore
Clear Candidate
Edit Candidate
Commit
Free Datastore

## Slide 24: Unlock the Running Datastore
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id=“6">
<unlock>
<target><running/></target>
</unlock>
</rpc>
Lock Datastore
Clear Candidate
Edit Candidate
Commit
Unlock Datastore
Notes: DEMO NOTE: 07_cmd-add-mpls-lsp-locking.py and 07_cmd-add-mpls-lsp-locking.xml applies here

## Slide 25: Validation and Rollback
I want to test the configuration before I commit and cancel out if necessary!
We will use:
The <validate> operation to validate the content of a datastore
The <commit> operation to commit candidate to running
  The <confirmed> parameter to denote a confirmed commit
  The <persist> parameter to specify a commit identifier
  The <confirm-timeout> parameter to specify a timeout before rollback

## Slide 26: Validation
<rpc message-id="5"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<validate>
<source>
<candidate/>
</source>
</validate>
</rpc>
Edit Candidate
Confirming Commit
...
Validate
Commit
Check for syntactical and semantic errors.
If ok is received back proceed to Commit

## Slide 27: Confirmed Commit
<?xml version="1.0" encoding="UTF-8"?>
<rpc message-id="6"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" >
<commit>
<confirmed/>
<confirm-timeout>10</confirm-timeout>
<persist>IQ,d4668</persist>
</commit>
</rpc>
Edit Candidate
Confirming Commit
...
Validate
Commit
Requires :confirmed-commit capability
Commit for 10 seconds then timeout and revert if confirmation not received

## Slide 28: Confirming Commit
<?xml version="1.0" encoding="UTF-8"?>
<rpc message-id="7"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" >
<commit>
<persist>IQ,d4668</persist>
</commit>
</rpc>
Edit Candidate
Confirming Commit
...
Validate
Commit
Notes: DEMO NOTE: 08_cmd-add-mpls-lsp-full.py and 08_cmd-add-mpls-lsp-full.xml applies here

## Slide 29: Configuring Multiple Devices
I want to configure multiple devices at once and rollback if anyone fails
This leverages a combination of parallel sessions and confirmed commits. We will use the same steps as in the previous example, but towards three network devices.
This allows for two-phase commit transactions

## Slide 30: Step #1: Prepare
Lock Datastore
Clear Candidate
Edit Candidate
Validate
Lock Datastore
Clear Candidate
Edit Candidate
Validate
Lock Datastore
Clear Candidate
Edit Candidate
Validate

## Slide 31: Step #2: Commit
Commit
Confirming Commit
Unlock Datastore
Commit
Confirming Commit
Unlock Datastore
Commit
Confirming Commit
Unlock Datastore

## Slide 32: Summary
You should now be able to:
Obtain desired configuration attributes from a device using NETCONF
Configure a network device using NETCONF
Understand NETCONF transactions